## Slide 1: Detecting potential temperature defects on harness of cables with reflectometry

## Slide 2
General context
  Needs for maintenance on RLV harnesses
  Reflectometry: a promising solution
  Problematics
New simulation model
  RLCG and ABCD description model
  Proposition for a new model
Experimental validation
  Cold spot detection
  Hot spot detection
  Comparison with simulation
Conclusion
Presentation Overview

## Slide 3
MRO costs are the key to reusable launch vehicles
COntext
https://callisto.cnes.fr/en/callisto-0
Cm: cost per mission
Cd: developpement costs
Cb: cost for construction
Nl: number of laucnhers per project
Nf: number of flight per launcher
Cmro: mro cost

## Slide 4
All cables are affected, from energy distribution to communication systems
ConStrainTS
Extreme temperatures
High levels of vibrations
Solar radiations
ACCIDENT

## Slide 5
Possible solutions
Harness replacement
Visual inspection
Offline monitoring
Online monitoring
FPGA solution

## Slide 6
Reflecometry on cables
  A defect will leave a trace on the voltage measurement
  The propagation time gives the distant to fault
  Harmlessness can be easily demonstrated
A CEA-CNES architecture was proposed in EUCASS-2019
Reflectometry

## Slide 7
CEA – CNES solution
Complex topology
Multiple access to media
Several types of defect
Limited access to sensors
Distributed sensors
TDMA
Several modes of monitoring
Small electronic architecture
+
analysis on the ground
Limitations
Technical solutions

## Slide 8
Previous work made only with simulations
problematics
Modeling method is not compatible with defect description
Models of temperature were not tested on real applications
 Need for a better simulation model
 Need for an experimental validation

## Slide 9
RLCG description
New simulation model
RLCG parameters are function of temperature

## Slide 10
New ABCD model
New simulation model
v
T1
T2
…
TN
Problems:
Additional reflections added by calculus
Computation time may explode

## Slide 11
Optimization of the model
New simulation model
Mesh-fineness:
Reflections mitigation: the thinner the better
Mesh-fineness:
Computation time: the larger the quicker

## Slide 12
Measurement devices
Experimental validation
CEA sensor:
Basis for an embedded system
Medium level of performances
Cheap
Dedicated to reflectometry measurements
Keysight VNA:
Reference device
High level of performances
Lab use only

## Slide 13
Cold spot detection
Experimental validation
Mastery over the temperature profile
Situation easy to reproduce in simulation

## Slide 14
Hot spot detection
Experimental validation
Mastery over the temperature profile
Situation easy to reproduce in simulation

## Slide 15
Comparison with simulation: cold spot
Experimental validation
VNA
CEA Sensor
Simulation

## Slide 16
Comparison with simulation: hot spot
Experimental validation
VNA
CEA Sensor
Simulation

## Slide 17
Great similarities between simulation and experiment
  Same behavior under temperature stress
  Position and relative magnitude respected
  Small undershooting of the model
  Validation of the new model
  Demonstration of the possibilities to detect temperature defect
Perspectives
  Reproduce and increase the parameters of the test
  Reduce the effect of test bed discrepancies
  Integrate the new model into simulation tools for whole systems
Conclusions

## Slide 18
THANK YOU FOR YOUR ATTENTION